## Slide 1: Unit 4: Faults in Rotating Machines and Diagnosis (16 L + 6 P hours)

## Slide 2: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Outlines:
Review of Machine Construction and Operation, Behavior of Normal Machines, Machine Condition Indicators.
Electrical Faults: Symmetrical Faults, Asymmetrical faults, Unbalance supply voltage, Over voltage, Phase reversal, Overload, Stator Short Circuit, Broken Rotor Bars and End-ring faults
Mechanical Faults: Airgap Eccentricity: Static, Elliptical, Dynamic and Mixed Eccentricity, Bearings Damage

## Slide 3: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Think Pair Share (5 minutes)
Discuss the constructional details of the induction motor.

## Slide 4: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Home Work- 1
List down all the components of induction motor and explain it briefly.
Explain the operation of induction motor.

## Slide 5: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Behavior of Normal Machines
Following are the important behavioral characteristics of the normal rotating machine like motors and generators:
1. Mechanical Behavior
Torque and speed characteristics will be normal
Vibrations will be under normal range
Machine will run with perfect balance
Operating sound will be within normal decibel
2. Electrical behavior
a) Voltage and current will be under normal condition
b) Efficiency of the machine will be perfect
c) Operates with high power factors

## Slide 6: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Thermal Behavior
Heat generation due to internal losses of the machine will be normal
Temperature rise in the machine will be with the limits
4. Dynamic Behavior
Stability of machine under varying load will normal
Starting and shutdown of the machine is smooth
5. Control System
Speed control will be very smooth
Position control will be highly precise

## Slide 7: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Machine Condition Indicators
Condition indicators for rotating machines are metrics used to assess their health and performance.
These indicators help in identifying potential issues early, allowing for predictive maintenance and preventing unexpected failures.

## Slide 8: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
1. Vibration Analysis
Overall Vibration Levels: Increased vibration levels often indicate imbalances, misalignment, bearing wear, or other mechanical issues.
Frequency Analysis: Identifying specific vibration frequencies can pinpoint the source of the problem, such as bearing faults or gear mesh issues.
Waveform Analysis: Time-domain analysis of vibration signals can detect transient events and irregularities in machine operation.

## Slide 9: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Temperature Monitoring
Winding Temperature: Elevated temperatures in motor windings can indicate overloading, insulation degradation, or cooling system failures.
Bearing Temperature: Monitoring the temperature of bearings helps in identifying lubrication issues or bearing wear.
Thermal Imaging: Infrared cameras can provide a visual representation of temperature distribution, revealing hot spots and areas of concern.
3. Lubrication Analysis
Grease Analysis: Similar to oil analysis, it helps in assessing the condition of greased bearings and detecting potential issues.

## Slide 10: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
4. Electrical Condition Monitoring
Current Analysis: Abnormal current levels or patterns can indicate electrical faults, such as winding short circuits or rotor bar issues.
Voltage Analysis: Voltage imbalances or fluctuations can affect machine performance and indicate electrical supply problems.
Power Factor: A declining power factor may signal inefficiencies or faults within the motor.
5. Acoustic Emissions
Sound Level: Changes in the sound level or unusual noises can be indicative of mechanical faults, such as bearing failures or misalignment.
Frequency Analysis: Analyzing the frequency spectrum of acoustic emissions can help in diagnosing specific issues.

## Slide 11: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
6. Motor Current Signature Analysis (MCSA)
Harmonic Analysis: Analyzing the harmonics in the current signature can detect issues like broken rotor bars, eccentricity, and bearing faults.
7. Insulation Resistance
Megger Testing: Measuring the insulation resistance of motor windings helps in detecting insulation degradation and potential short circuits.

## Slide 12: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Electrical Faults: Symmetrical Faults, Asymmetrical faults, Unbalance supply voltage, Over voltage, Phase reversal, Overload, Stator Short Circuit, Broken Rotor Bars and End-ring faults
Failures is an event that results complete or partial loss of the object functionality.
1. Diagnosis (detection of cause)
Identification of the fault by monitoring symptoms.
Examples:
Detection of certain harmonics in frequency spectrum
Voltage is unbalanced
Phase is dropped

## Slide 13: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Reliability is an ability of an object to perform desired operation and sustain it with in a defined interval of time.

## Slide 14: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
WEIBULL MODEL

## Slide 15: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Asymmetrical faults:
Phase-to-Ground 70% a)
Phase-to-Phase 15% b)
Two Phases to Ground 10% c)
Phase to Phase and Phase to Ground 2-3% d)

## Slide 16: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Asymmetrical faults:
e) Three Phases Short Circuited 2-3% e)
f) Three Phases to Ground 2-3% f)

## Slide 17: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.

## Slide 18: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Unbalance Supply Voltage
Unbalanced supply voltage in an electric motor occurs when the voltages in a three-phase system are not equal or when the phase angles between the voltages are not 120 degrees apart.
Effects of Unbalanced Supply Voltage
Increased Heating:
Motors running on unbalanced voltage can experience excessive heating, leading to insulation failure and reduced lifespan.
2. Reduced Efficiency:
Unbalanced voltages cause the motor to draw more current, reducing its efficiency.
3. Vibration and Noise:
Voltage imbalance can cause mechanical stress and result in increased vibration and noise.

## Slide 19: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
4. Reduced Torque:
The motor may not produce the rated torque, leading to poor performance in applications requiring constant torque.
5. Overcurrent:
Unbalanced voltages can cause one or more phases to draw excessive current, tripping protective devices.
6. Rotor Damage:
Prolonged exposure to unbalanced voltages can cause damage to the rotor, particularly in squirrel cage motors.

## Slide 20: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Over Voltage Faults in Electrical Machines
Over voltage is caused by lightning strikes, switching surges, poor voltage regulations, unbalanced loads and harmonic distortions.
Effects of Overvoltage
Effects of overvoltage in electrical machines can cause insulation damages, over heating in windings, mechanical stresses and reduce life span of the machines.

## Slide 21: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Over Voltage Faults in Electrical Machines
Over voltage is caused by lightning strikes, switching surges, poor voltage regulations, unbalanced loads and harmonic distortions.
Effects of Overvoltage
Effects of overvoltage in electrical machines can cause insulation damages, over heating in windings, mechanical stresses and reduce life span of the machines.

## Slide 22: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Other Faults in Electrical Machines:
Phase reversal,
Overload,
Stator Short Circuit,
Broken Rotor Bars and
End-ring faults

## Slide 23: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Stator Short Circuit,
Stator and armature faults are related to insulation failures in electrical machines .
These faults can be classified as winding failures and stator lamination stack short-circuits.
Regardless of the main cause of the winding fault, the actual mode of the failure can be divided down into five groups, which are illustrated in figure shown below.
A failure in the machine stator can start with a minor turn-to-turn short circuit within one coil.
When this fault is not detected and treated, it will propagate, and excessive heat is generated within the shorted coil.
This will result in insulation deterioration and at some point, in a partial ground short-circuit through the slot liner.

## Slide 24: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
The main symptoms of the stator faults can be found in several publications
These can be:
high stator core or winding temperatures;
slack core lamination, slot wedges, and joints;
loose bracing for end winding;
electrical discharges;
leakage in the cooling system.

## Slide 25: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Other Faults in Electrical Machines:
Broken Rotor Bars

## Slide 26: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Broken Rotor Bars
The electric current that is induced by the stator field, flows through the rotor bars.
It is producing a magnetic force that will create necessary torque in the machine.
Rotor bars that might crack, break or separate from the end rings prevent current to flow, which in hand limits motor performance.
As a result, there is a thermal difference in the rotor, a lack of induced magnetic field, an unbalanced radial force and vibration components.
Main reasons for such types of faults are:
thermal stresses because of thermal overload, unbalance, hot spots or excessive losses, sparks, etc.;
magnetic stresses by unbalance magnetic pull, vibration;
dynamic stresses arising from shaft torques, centrifugal forces and cyclic stresses;
mechanical stresses because of loose lamination, fatigued parts, or bearing failure.

## Slide 27: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Other Faults in Electrical Machines:
Phase reversal,
Overload,
Stator Short Circuit,
Broken Rotor Bars and
End-ring faults

## Slide 28: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Common Mechanical Faults
Stator faults (loosen core and windings, insulation failure etc.)
Rotor faults (broken rotor bars and end ring cracks, shaft bending and cracks etc.)
Eccentricity (missed alignment between stator axis and rotor shaft axis)
Bearing faults (bearing current, heating and improper lubrications, electric arching, cotamination and corrosions)
Overload couplings (over loading)
Winding insulation faults (excess heating, aging and environmental factors)
Loosen core

## Slide 29: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Common Environmental Faults
Ambient high/low temperature,
2. Cooling system failure,
3. Moisture,
4. Dust and dirt,
5. Vibrations due to bad foundation…
Loosen core

## Slide 30: As learners, we must put more of an emphasis on LISTENING than on working alone!
Thanks to Mrs. Karolina Kudelina and Professor Toomas Vaimann