## Slide 1: Unit 4: Faults in Rotating Machines and Diagnosis (16 L + 6 P hours)

## Slide 2: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Outlines:
Machine Testing and Fault Diagnostics: Fault Indicators and Fault Representing Equations
Bearing Currents and it’s diagnosis:
i. Indirect methods: Vibration, ultrasonic detection, and
ii. Direct methods: voltage measurement, Rogowski Coil;
3. Reduction of bearing currents: Insulated bearings, conductive greases, shaft grounding contacts and rings, characteristics regulation of frequency converters

## Slide 3: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Machine Testing and Fault Diagnostics: Fault Indicators and Fault Representing Equations
Common Fault Indicators Include:
Electrical Systems:
Voltage Drop: Sudden drops in voltage levels can indicate faults such as short circuits or overloads.
Current Spike: Unusually high current can indicate faults such as short circuits or insulation failures.
Harmonics: Presence of harmonic distortions can indicate issues like transformer saturation or non-linear loads.

## Slide 4: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Mechanical Systems:
Vibration: Excessive vibration can indicate mechanical imbalance, misalignment, or bearing faults.
Temperature: Overheating can indicate lubrication issues, friction, or electrical faults.
Noise: Unusual noises can be a sign of mechanical wear, misalignment, or other mechanical failures.
3. Process Control Systems:
Pressure Variations: Sudden changes in pressure can indicate blockages, leaks, or pump failures.
Flow Rate Changes: Deviations in flow rates can signal pump issues or obstructions in pipelines.
Chemical Composition: Changes in chemical composition can indicate leaks, contamination, or process disturbances.

## Slide 5: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Fault Representing Equations
Every fault in any electrical equipment leaves certain frequency components in its associated signals such as current, voltage, speed, torque and flux, etc.
In case electrical machines the most common faults modulate the current spectrum by following frequencies.

## Slide 6: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Where,
k is an integer,
is the number of rotor bars, for static eccentricity and in case of dynamic eccentricity,
S is the slip, V = 1, 2, 3… represents the supply harmonics and
P is the number of pole pairs,
, is the number of bearing balls,
is the rotor’s mechanical frequency,
m is a positive integer,
is the bearing pitch diameter,
is the bearing ball’s diameter and
θ is the angle between ball and races.

## Slide 7: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Bearing Currents and it’s diagnosis
Indirect methods: Vibration, ultrasonic detection, and
Direct methods: voltage measurement, Rogowski Coil;
What is mean by bearing current ?
Bearing current refers to electrical currents that flow through the bearings of rotating machinery, such as electric motors or generators.
This phenomenon can lead to damage and premature failure of the bearings.

## Slide 8: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Determining the presence of bearing currents in electric machines is possible only through two methods:
Visual inspection of bearings after failure.
Detection of bearing currents through measurement.
These methods of detecting bearing currents can be further divided into two major subgroups.

## Slide 9: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
INDIRECT METHODS
Indirect methods can only identify bearing currents in electric machines when the race surfaces are already damaged due to bearing currents.
The moving elements on the damaged surfaces generate vibration and noise, which is when these currents become detectable through indirect methods.
Additionally, detecting bearing currents in the early stages of damage using indirect methods requires significant expertise and training.
There are various types of damage that can occur in rolling bearings, and the vibration spectra of damaged bearings can be relatively similar in the early stages of damage.
Even with experienced specialists who can identify the vibration caused by bearing current damage in the early stages and immediately minimize the currents, the damaged bearings still need to be replaced prematurely.
This is because iron particles have entered the lubricant, the lubricating properties of the lubricant have deteriorated, and the race surfaces of the bearings have been damaged.
If the presence of bearing currents is detected using a stethoscope or the human ear, the condition of the rolling bearings is usually already critical.
In such cases, the bearings should be replaced as soon as possible.

## Slide 10: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
INDIRECT METHODS
1. Vibrations
Before failure, the vibration spectrum of bearings is usually exponentially increasing.
The increase in vibration due to bearing currents is also exponential before failure.
The defect caused by bearing currents is distributed evenly on the race surfaces, and as the vibration increases, the bearing starts making loud noises.
Therefore, bearings damaged by bearing currents are typically replaced before complete failure to prevent catastrophic breakdowns.

## Slide 11: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
INDIRECT METHODS
2. Stethoscope
The simplest and widely used tool for checking the condition of electric machines and transmission mechanisms (through noise or vibration inspection) is a stethoscope.
Modern stethoscopes are electronic, and additional features may include:
Digital volume control: Allows for precise adjustment of the volume.
Sound recording: Enables the recording of sounds for further analysis.
Use of various filters (high-frequency, mid-frequency, low-frequency): This feature allows for better classification and localization of sounds emanating from bearings, ultimately providing a more precise definition of the nature of the defect.

## Slide 12: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
INDIRECT METHODS
3. Ultrasonic Detection
Indirect methods suitable for detecting motor bearing currents work well with ultrasonic detectors.
The method of determining the condition of bearings using ultrasonic detection originated from NASA test laboratories, where relationships between the condition of rolling bearings and the ultrasonic frequencies emitted by the bearings were discovered during the testing of aerospace technology.
Similar to vibration analysis, ultrasonic spectrum analysis reveals peaks in the sound frequencies generated by the damage to the race surfaces of the bearings due to bearing currents.
In addition to data analysis, an ultrasonic detector can also be used to listen for bearing defects, similar to how a stethoscope is used.

## Slide 13: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
DIRECT METHODS
When detecting motor bearing currents, direct measurement methods should always be preferred because only through them can the presence of bearing currents be immediately discovered after the electric machines are started or activated.
Immediate or very early detection of bearing currents, coupled with the implementation of appropriate countermeasures based on the nature of the problem, creates opportunities for preventing bearing damage.
Detecting the sparking events occurring in the rolling bearings of electric machines due to bearing currents through direct measurement has been quite complicated until the last decade.
In addition to complex measurement procedures and instruments, access to all (more powerful) electric machine shafts and other moving details is limited due to safety regulations, as they are always securely covered for safety reasons.
Only with the advent of new-generation measurement instruments can bearing currents be quickly, safely, and remotely detected without direct physical contact with the measured electric machine.

## Slide 14: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
DIRECT METHODS
MULTIMETER
For measuring the voltage on the motor shaft, it is advisable to choose a multimeter with a high input resistance, as the higher the input resistance of the multimeter, the more accurate the measurement results will be.
If the multimeter shows an alternating voltage below 100 mV (for motors with roller bearings, and below 200 mV for sliding bearings), it can be assumed that the motor bearings are not at risk.
However, if the measurement result approaches or exceeds one volt, it may indicate a risk to the motor bearings.
This is because sparking events may occur in the bearings due to bearing currents, and the low electrical resistance of the shaft can lead to currents of tens of amps with just a few hundred millivolts of voltage between the ends of the shaft.

## Slide 15: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
DIRECT METHODS
2. OSCILLOSCOPE
A universal and practical measurement device that provides the best overview of various bearing currents in a motor (their shape and parameters) is an oscilloscope.
In general, when sparking events occur, the voltage range is typically ±20…80 V, with the voltage increasing in about 10 µs (during this time, the current in the bearing is around 0 A).
The duration of a bearing sparking event is a few nanoseconds, during which the current in the bearing reaches its maximum.
Since placing the measurement probe of the oscilloscope in direct contact with the motor shaft is required for measuring the shaft voltage, all safety precautions must be followed during the measurement.
In addition to moving parts, in large motors with insulated bearings, the voltage between the shaft and the housing can become dangerously high, so it is essential to check the voltage on the shaft with a multimeter before starting oscilloscope measurements to ensure safety.

## Slide 16: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
DIRECT METHODS
3. ROGOWSKI COIL
A widely used, simple, and safe method for measuring three-phase current and motor shaft current is the use of instruments based on the Rogowski coil or loop principle.
When measuring three-phase current, the Rogowski coil must be placed only around the motor power cables (it should not encircle the neutral cable), and when measuring shaft current, it should be placed around the motor shaft.
The instantaneous voltage across the terminals of the Rogowski coil is proportional to the derivative of the instantaneous primary current, and since the secondary current needs to be determined by integrating the secondary voltage, an integrator is always connected to the output of the air-core current transformer.
The need for this can be considered one of the main drawbacks of the Rogowski coil.
The Rogowski coil is sensitive to noise, so attention must be paid to electromagnetic compatibility.

## Slide 17: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.

## Slide 18: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Reduction of bearing currents: Insulated bearings, conductive greases, shaft grounding contacts and rings, characteristics regulation of frequency converters
Introduction
Strategies for reduction of bearing currents can be divided into three major categories:
Insulating and conductive components (insulated bearings and shafts, conductive grease, grounding brushes),
Non-motorized measures (filters, ground, magnetic coupling, frequency converter parameters),
Motor reconstruction (Faraday shielding, increase of rotor impedance).

## Slide 19: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
1. Insulated Bearings
In motors controlled by frequency converters, shaft currents have the greatest effect on the motor bearings, where the bearing surfaces are damaged quickly and irreversibly by spark discharges.
In this case, the lifespan of the bearing is determined by the number of spark solutions and their intensity.
As a result, bearing can deteriorate tens of times faster. bearing can deteriorate tens of times faster.
The larger the device, the more complicated and expensive it is to replace the motor bearings.

## Slide 20: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Insulated Bearings
In the case of motors with a power of more than 100 kW, to reduce bearing currents, there are recommended following solutions in priority order:
Insulated bearings,
Insulated shaft,
Insulated housing of the bearing,
Insulated rings,
Hybrid bearings,
Ceramic bearings,
Magnetic bearings.

## Slide 21: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Insulated Bearings
The most common method to eliminate the bearing currents is to use insulated bearing(s).
An insulated bearing is a completely ordinary steel bearing, which inner and/or outer rings are covered with a ceramic material.
Usually, this material consists largely of alumina (Al2O3).
An insulated bearing is 5…10 times more expensive than a common bearing.
Since the usage of an insulated bearing increases the price of the electrical machine by ~15%, insulated bearings are usually not included in the standard equipment of smaller motors.
Many of motor manufacturers provide solutions for the reduction of bearing currents with the usage of only one insulated bearing.
This solution can help to reduce the high-frequency shaft currents circulating in the motor.
In the case of motor failure, it is also advisable to replace the insulated bearing in order to reduce the risks associated with the dismantling and installation.

## Slide 22: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Insulated Bearings
If the motor has two insulated bearings, the following should be considered:
There is a potential difference between the motor shaft and the housing, which can be up to 10% of the motor supply voltage, or in some cases even greater, as shown in graph.
Shaft voltage can be dangerous to people and to motor-related equipment (such as a tachometer or equipment connected to the motor shaft).
Purchasing a new motor controlled by a frequency converter, it can be reasonable to choose a motor with an insulated shaft instead.

## Slide 23: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Insulated Bearings
Only in case of ceramic, hybrid or magnetic bearings, shaft currents can be completely avoided.
As common metal bearings, the housings of hybrid bearings are made of metal. However, the rolling elements are usually made of ceramic.
The housing of hybrid bearing is made of metal, while the housing of ceramic bearing is made of ceramics.
Magnetic bearings have many advantages over the common bearings, some of them are as follows:
No vibration,
Lubrication is not required,
No friction,
Can be used at high speeds (up to 40 000 rpm),
Extended lifespan.

## Slide 24: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Conductive Greases
The generation of bearing currents and their magnitude in motor bearings are directly related to the dielectric properties of the lubricant used.
Generally, bearing lubricants can be conditionally classified as follows:
Conductive greases, which have electrical resistivity in the range … Ω·cm,
Non-conductive greases, which have electrical resistivity in the range … Ω·cm.
If there are used lubricants with low electrical resistivity, the bearing capacity is relatively small and their electrical conductivity is generally sufficient to direct the currents to flow them from the rotor to the motor housing safely and without damaging the bearings.
To increase the electrical conductivity, metallic dust is added to the lubricant, which reduces the relative dielectric constant of the lubricant by 1000 times.

## Slide 25: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Conductive Greases
Using conductive greases, it must be considered these greases shorten the lifespan of the bearing by about three times.
Because of the extremely abrasive conductor debris contained in the grease, microcracks are to be created on the bearing surface, especially in case of high rotational speed.
Besides, electrical conductivity of the lubricant is not constant and depends on the operating conditions changing over the time.

## Slide 26: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Conductive Greases
Although the use of a conductive lubricant is the cheapest and fastest way to solve the problem of bearing currents, this method may be recommended rather than a temporary solution.
Due to the spark solutions, metal debris is released from the bearing surface, which gets into the lubricant and significantly increases the electrical conductor properties of the lubricant.
During sparking, the lubricant and impurities oxidize, causing the grease to darkening, shorten the life of the lubricant and degrade lubrication properties.

## Slide 27: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Shaft Grounding Contacts and Rings
Basically, there are two methods to protect the motor controlled by frequency converters from shaft currents and spark solutions are:
Dielectric separation between the motor shaft and the housing so that the bearings cannot pass through the bearings,
Creation of electrical connection between the motor shaft and the housing, for which the shaft grounding contacts and rings are well suited.
The operating principle of grounding contacts is identical to the brushes used to feed the windings of the DC motor.
The lifespan of the brushes is mostly determined by the compressive force of the electrical transmission with which the brush is pressed against contact.
The higher the pressure, the faster the brush wears.
Grounding rings are made from hundreds of thousands to millions of carbon fibers, which are only a few microns in diameter and about ten millimeters in length.

## Slide 28: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Shaft Grounding Contacts and Rings
Grounding contacts can have an uneven electrical contact. In this case, brushes are to be changed and monitored constantly.
The installation of the grounding ring is not more complicated than the grounding contact.
However, since the microfibers of the grounding ring are in minimal contact with the shaft (or there is no direct contact), it is recommended to cover the fibrous part of the motor shaft under the grounding ring with a special conductive silver paint.

## Slide 29: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
4. CHARACTERISTICS REGULATION OF FREQUENCY CONVERTERS
Basically, bearing currents can be caused by the following non-adjustable technical characteristics of the frequency converter:
  Frequency converter power electronics (design and components),
  Presence of built-in filters,
  PWM topology,
  Frequency converter power supply type.
  Operating principle of frequency converter (frequency control or vector control).
The number of power electronics output stages in the frequency converter has the largest and most decisive effect on the generation of bearing currents.
The vast majority of frequency converters used in industry are two-level, but already at the output of a three-level frequency converter, which minimize or even eliminate the risk of spark discharges in motor bearings.

## Slide 30: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
4. CHARACTERISTICS REGULATION OF FREQUENCY CONVERTERS
Although multilevel frequency converters significantly reduce motor leakage currents, multilevel inverters are very expensive, so it may still be more economical to choose a two-level inverter with integrated filters to reduce shaft currents and interference.
Standardly, there are used the following filters:
  dU/dt filter,
  Sine wave filter,
  Filter for reduction of higher harmonics,
  EMC filter.

## Slide 31: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
4. CHARACTERISTICS REGULATION OF FREQUENCY CONVERTERS
Purchasing a new frequency converter, it is recommended to choose the PWM topology, which allows to reduce the generation of shaft currents (switching frequency is supposed to be low).
For example, Soft-Switching PWM is suitable, which allows the motor to be operated at a relatively low switching frequency.
In theory, there are also proposed many different PWD methods have been proposed, such as Zero Common-Mode PWM (ZCM), Zero Common-Mode Subharmonic PWM (ZCM-SPWM), Active-Zero-State (AZS), Remote-Three-State (RTS), Nearest-Three-State (NTS).
However, different strategies can degrade the efficiency of the frequency converter or increase the higher harmonic generation.
Due to what these algorithms have not found practical usage.

## Slide 32: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Comparison

## Slide 33: As learners, we must put more of an emphasis on LISTENING than on working alone!
Thanks to Mrs. Karolina Kudelina and Professor Toomas Vaimann

## Slide 34: As learners, we must put more of an emphasis on LISTENING than on working alone!
Reference: