## Slide 1: Unit 5: Condition Monitoring and Condition Based Maintenance (10L + 5P hours)

## Slide 2: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Outlines:
Types of Maintenance: Breakdown vs. Condition Based Maintenance; Scheduled, Preventive and Predictive maintenance;
Condition monitoring and signal processing for state of health and fault indications.

## Slide 3: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Types of Maintenance:
1. Breakdown vs. Condition Based Maintenance

## Slide 4: As learners, we must put more of an emphasis on LISTENING than on working alone!
Breakdown Versus Condition-based-maintenance.
a. Breakdown Maintenance (Reactive Maintenance)
1. Unplanned:
Maintenance activities are not scheduled; they occur in response to equipment failure.
2. Immediate Action Required:
Repairs need to be carried out immediately to minimize downtime.
3. Higher Downtime:
Equipment downtime is typically longer because repairs are unplanned and may require time to diagnose and fix the issue.

## Slide 5: As learners, we must put more of an emphasis on LISTENING than on working alone!
Breakdown Versus Condition-based-maintenance.
a. Breakdown Maintenance (Reactive Maintenance) cont…
4. Higher Cost:
Often leads to higher costs due to emergency repairs, overtime labor, and potential secondary damage to equipment.
5. Limited Life Cycle Management:
Focus is on immediate fixes rather than extending the overall life of the equipment.

## Slide 6: As learners, we must put more of an emphasis on LISTENING than on working alone!
Breakdown Versus Condition-based-maintenance
b. Condition-Based Maintenance (CBM) (Predictive Maintenance)
Planned and Predictive:
Maintenance is scheduled based on the actual condition and performance data of the equipment.
2. Monitoring and Analysis:
Utilizes sensors, diagnostics, and data analysis tools to monitor equipment health.
3. Reduced Downtime:
Maintenance can be planned and performed before a failure occurs, reducing unplanned downtime.

## Slide 7: As learners, we must put more of an emphasis on LISTENING than on working alone!
Breakdown Versus Condition-based-maintenance.
2. Condition-Based Maintenance (CBM) (Predictive Maintenance) cont…..
4. Optimized Maintenance Intervals:
Maintenance activities are performed only when necessary, extending equipment life and reducing unnecessary maintenance.
5. Higher Initial Investment:
Requires investment in monitoring systems and technology.

## Slide 8: As learners, we must put more of an emphasis on LISTENING than on working alone!
Merits and Demerits of Breakdown Versus Condition-based-maintenance
 | Break Down | Condition based
Advantages | Simplicity | Improved Reliability
 | Short-term cost saving | Better Resource Allocation
Disadvantages | Unpredictability | Higher Initial Costs
 | Higher Long-Term Costs | Complexity

## Slide 9: As learners, we must put more of an emphasis on LISTENING than on working alone!
Types of Maintenance:
2. Scheduled Maintenance
Definition of Scheduled Maintenance: Regularly planned maintenance activities to prevent unexpected equipment failures and ensure optimal performance.
Types:
Preventive Maintenance: Routine inspections and servicing based on time intervals or usage.
Predictive Maintenance: Maintenance activities based on real-time data and condition monitoring.
Time-Based Maintenance: Scheduled at fixed intervals (daily, weekly, monthly, annually).
Usage-Based Maintenance: Based on the actual use of equipment (e.g., every 1000 hours of operation).

## Slide 10: As learners, we must put more of an emphasis on LISTENING than on working alone!
Types of Maintenance:
2. Scheduled Maintenance
Tools and Techniques:
Condition Monitoring Tools: Vibration analysis, thermography, oil analysis.
Computerized Maintenance Management Systems (CMMS): Managing maintenance schedules, tracking work orders, and maintaining records.
Checklists: Standardized lists to ensure all steps are followed.

## Slide 11: As learners, we must put more of an emphasis on LISTENING than on working alone!
Types of Maintenance:
3. Preventive Maintenance
Traditional types of maintenance can be generally classified into two categories: Corrective and Preventive Maintenance.
In the case of corrective maintenance, also known as reactive maintenance, all needed control and repairs are assumed to the equipment after the failure has already occurred.
At the same time, it is possible to assume preventive maintenance to the electrical equipment in order to avoid catastrophic outcomes.
In this case, the electrical equipment needs to be regularly checked through scheduled and specified inspections.

## Slide 12: As learners, we must put more of an emphasis on LISTENING than on working alone!
Types of Maintenance:
3. Preventive Maintenance cont…
Unfortunately, aforementioned maintenance types are not suitable for industry, as both of them have a substantial economic impact.
In the case of corrective maintenance, the equipment is already damaged or broken, disrupting the process.
In case of preventive maintenance, there is a possibility that equipment is about to be broken in near future, which also will have a negative impact of operation.

## Slide 13: As learners, we must put more of an emphasis on LISTENING than on working alone!
Figure 1: Maintenance types: a) corrective maintenance and b) preventive maintenance

## Slide 14: As learners, we must put more of an emphasis on LISTENING than on working alone!
Types of Maintenance:
4. Predictive Maintenance
To minimize downtime due to scheduled checks and decrease shutdown costs, manufacturers apply predictive approaches to the production.
In this case of predictive maintenance, condition monitoring is a crucial component that allows to forecast a potential damage based on working conditions of electrical equipment.
A schematic illustration of the predictive maintenance is shown in Figure 2.

## Slide 15: As learners, we must put more of an emphasis on LISTENING than on working alone!
Figure 2: The idea of predictive maintenance

## Slide 16: As learners, we must put more of an emphasis on LISTENING than on working alone!
Types of Maintenance:
4. Predictive Maintenance cont…
Due to huge amount of data and numerous parameters to be monitored, it is reasonable to use for diagnostics and condition monitoring, artificial neural networks have been considered as an effective tool.
Due to their non-linearity and extremely good adaptivity, neural networks are able to make precise predictions.
Neural networks deal with classification, prediction, and recognition, so they can out-perform nearly every machine learning algorithm.
Artificial neural networks reproduce biological nervous systems as well as its ability to learn and correct errors by modeling the brain’s low-level structure.
To build an artificial structure, it is needed to create a system with a similar structure as biological one.

## Slide 17: As learners, we must put more of an emphasis on LISTENING than on working alone!
Condition Monitoring and Signal Processing for State of Health and Fault Indications.
Condition monitoring involves the continuous or periodic assessment of equipment health to detect potential faults early.
Signal processing for state of health (SoH) involves analyzing and interpreting signals from equipment to assess its condition and predict potential failures.
Signal processing for fault indications involves analyzing and interpreting signals from equipment to detect, diagnose, and predict faults.

## Slide 18: As learners, we must put more of an emphasis on LISTENING than on working alone!
Condition Monitoring and Signal Processing for State of Health and Fault Indications.
Fault Detection and Diagnosis:
Pattern Recognition: Identifying known fault patterns in the signal data.
Anomaly Detection: Identifying deviations from normal operating conditions that may indicate potential issues.
Classification Algorithms: Machine learning models that categorize signal data into normal and faulty states.
Regression Models: Predicting the severity of faults and remaining useful life (RUL) of equipment.

## Slide 19: As learners, we must put more of an emphasis on LISTENING than on working alone!
Condition Monitoring and Signal Processing for State of Health and Fault Indications.
Machine Learning and AI: Algorithms trained on historical data to classify and predict faults.
Techniques include:
Support Vector Machines (SVM)
Artificial Neural Networks (ANN)
Deep Learning Models

## Slide 20: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Figure 3: Overview of Sensors, data acquisition and Signal Pre-processing in condition monitoring

## Slide 21: As learners, we must put more of an emphasis on LISTENING than on working alone!
References: