## Slide 1: Unit 5: Condition Monitoring and Condition Based Maintenance (10L + 5P hours)

## Slide 2: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Outlines:
Recent Trend in Condition Based Maintenance: Remote sensing and cloud based monitoring and
Maintenance management : Internet of Things (IoT), IoT Based Sensing,
Application of Machine Learning and Artificial Intelligence for Maintenance, Use of trained models for anomaly detection and fault diagnosis.
Commercial CMMS (Cloud/computer based maintenance management system), CMMS Architecture and Interface, Use of CMMS

## Slide 3: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Recent Trend in Condition Based Maintenance: Remote sensing and cloud based monitoring and
The recent trend in condition based monitoring and maintenance are such as:
1. Digital Twins
2. Remote sensing and monitoring
3. IoT and
4. Cloud computing etc.
5. Artificial Intelligence

## Slide 4: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
1. Digital Twins
Is an integrated multi-physics, multiscale, probabilistic simulation of a system that uses the best physical models, sensors, fleet history, etc., to simulate the life of its corresponding physical twin by (by National Aeronautical Space Administration (NASA))
Chen, defined as a computerized model of a physical system that mirrors its functional features.
Zheng et al. said that DT is a virtual information set that describes actual physical assets.
Mandi, defined DT as a virtual instance of a physical system (twin) continually updated with the latter's performance, maintenance, and health status data throughout the physical system's life cycle.

## Slide 5: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
1. Digital Twins
DTs' also known as computational mega-models, mirror systems, or avatars, can be defined as a digital representation of a physical object, process, or service. A DT can be a digital replica of an object in the physical world, such as a jet engine or wind farm, or even larger items such as buildings or even whole cities. As well as physical assets, the DT technology can replicate processes to collect data to predict how they will perform.
A DT is, in essence, a computer program that uses real-world data to create simulations that can predict how a product or process will perform. These programs can integrate the IoT, artificial intelligence, and software analytics to enhance the output.

## Slide 6: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 1: DT system

## Slide 7: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 2: DT Applications

## Slide 8: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring
With the recent advancements in information technology, industries are moving towards predictive and proactive maintenance from periodic and reactive maintenance.
Different stages of maintenance phases for industrial equipment is shown in Figure 3.
This helped monitor the electrical equipment in real-time and gather data from the equipment to develop algorithms for fault prediction.
Figure 3: Maintenance phases of electrical equipment

## Slide 9: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring Cont…
This combination of information technology with electrical devices changed the landscape of fault detection and prediction in electrical machines.
The implementation of smart devices for industrial applications has further streamlined the industrial process and made it easier for end users to determine the issues with the monitored electrical equipment if any.
These smart devices can communicate with each other and implement logical decisions based on incoming data.
The setup of these smart devices over a network (e.g. the internet) is termed as Internet of Things (IoT).
The monitoring of electrical equipment with the help of IoT and cloud in real-time is usually known as Remote Sensing or Monitoring.

## Slide 10: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring Cont….
IoT has become one of the norms of modern industry and transformed itself into one of its strongest pillars.
Along with IoT, another vital aspect of predictive maintenance is machine learning trained algorithms for fault detection and prediction.
Classification of incoming signals to detect whether it is healthy or faulty requires the trained model to be highly accurate.
To improve the accuracy of the machine learning trained model, it is necessary to focus on the quality and quantity of data samples provided for training.
It is also essential to optimize the machine learning algorithm for training to get the best possible trained model.
The most commonly used classification algorithms are Artificial Neural Networks (ANNs).

## Slide 11: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring Cont…
Machine learning algorithms are primarily implemented for fault diagnostics nowadays because it is easier to implement the trained model in real-time.
As it is most difficult to get high quality data in quantity using experimental setups, researchers are devising new ways to gather data for different faults using simulations or statistical equations.
Similarly, data from experimental setups and real-life implemented systems are also being gathered using condition monitoring systems.

## Slide 12: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring Cont…
Currently, most of the systems used are developed in SCADA or PLC , which are expensive, hard to transport and complex to use.
Researchers are now looking into other condition monitoring systems that can replace current systems and are cost-efficient.
For this purpose, researchers are looking into developing microcontroller cards and developing condition monitoring systems based on them.
The general implementation of a condition monitoring system in an industrial application is shown in Figure 4.

## Slide 13: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 4: Industrial application of condition monitoring system

## Slide 14: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring Cont…
Here the data is read from the electrical machine through sensors which is then forwarded onto the control center or cloud using a data acquiring system.
The cloud then runs any analysis that is needed to be done on the incoming data for the detection of faults and the processed data is then shown on a GUI for the end user.
This makes it easier for the user or technician to monitor the health of the electrical machines and to identify if those machines need maintenance or not.
This is a general example of a condition monitoring system in terms of an industrial application.

## Slide 15: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Remote Sensing and Monitoring Cont…
Although many microcontroller cards are available now, some of the most easy-to-use and stable ones include Arduino UNO, Arduino MEGA, Teensy 4.0, ESP32, and Raspberry Pi.

## Slide 16: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 5: Schematic main field of Industry 4.0

## Slide 17: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 6 Composition of the fault detection system

## Slide 18: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 7: Classification of fault diagnostic techniques

## Slide 19: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Artificial Intelligence
The industry 4.0 revolution focuses on merging information technology with industry applications.
This has resulted in condition monitoring and predictive maintenance is considered a crucial part of modern industry.
Nowadays, most of the electrical machines and drive systems in the industry play significant roles in many applications.
Abrupt halt or unattended faults to these machines and drives can lead to further disaster on a bigger scale.
That is why scheduled maintenance is being carried out for these machines and drives, which is not very cost efficient.
Artificial intelligence has played a vital role in minimizing the loss of such machinery and making its maintenance more cost-efficient.
Today there are plenty of condition monitoring methods available to detect faults in electrical equipment and machines.
Generally, these diagnostic methods can be divided into the following groups:

## Slide 20: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Artificial Intelligence Cont…
Noise and vibration monitoring,
Motor-current signature analysis (MCSA),
Temperature measurement,
Electromagnetic field monitoring,
Chemical analysis,
Radio-frequency emissions monitoring,
Acoustic noise measurement,
Model and artificial intelligence-based techniques

## Slide 21: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Artificial Intelligence Cont…
It is important to identify the faults generated due to these stresses in time as it can damage the electrical machine and motor to the extent that it breaks down.
This is where machine learning algorithms come into play.
These algorithms train models based on the data collected from electrical machines and drives, which help us detect faults in their initial stages.
This helps to reduce the damage and also to identify the faults, which need immediate attention.
This is generally known as condition monitoring of electrical machine.

## Slide 22: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Artificial Intelligence Cont…
Many studies and research work about intelligent condition monitoring are referred to machine learning.
Machine learning can be defined as a study of artificial intelligence and computer science, which is not oriented directly to solving of a problem but rather learning in the process by applying solutions to other similar problems.
Generally, machine learning can be classified by the way the model is to be trained.
It can be supervised, unsupervised, semi-supervised, and reinforcement.

## Slide 23: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
3. Artificial Intelligence Cont…

## Slide 24: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Table 1: Comparison of the main algorithms for condition monitoring

## Slide 25: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Table 1: Comparison of the main algorithms for condition monitoring

## Slide 26: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Figure 8: Conceptual schematic view of different areas of AI in Industry 4.0

## Slide 27: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Machine Learning -- Python Examples
Decision Trees
The first part is to load the libraries needed for the program, here sklearn and matplotlib libraries are loaded up.
After this, the data is loaded into the variables and the classifier is selected.

## Slide 28: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Machine Learning -- Python Examples
Decision Trees
The input data is fitted into the classifier and the resultant tree is being plotted.
This will show the result in decision tree format after the data is fitted into the classifier.

## Slide 29: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Machine Learning -- Python Examples
Decision Trees
The above model classifies the data according to the condition and value into correct dataset together.
It works as branching it out to reach the correct classification with decisions of yes or not.
This is one of the simplest classifications in machine learning algorithms and is usually used for less complex scenarios.

## Slide 30: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Commercial CMMS (Cloud/computer based maintenance management system), CMMS Architecture and Interface, Use of CMMS
A Commercial Computer-Based Maintenance Management System (CMMS) is a software platform designed to streamline maintenance operations, improve asset management, and enhance overall operational efficiency.
Benefits of Implementing a CMMS:
Improved Efficiency: Streamline maintenance operations, reducing downtime and increasing productivity.
Cost Savings: Optimize inventory management and reduce unnecessary maintenance expenses.
Enhanced Asset Lifespan: Prolong the life of equipment through regular and predictive maintenance.
Regulatory Compliance: Ensure compliance with industry regulations and standards.
Data-Driven Decisions: Make informed decisions based on comprehensive data analysis and reporting.

## Slide 31: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Commercial CMMS (Cloud/computer based maintenance management system), CMMS Architecture and Interface, Use of CMMS
Popular CMMS Software:
IBM Maximo: Known for its extensive features and scalability.
SAP EAM: Part of SAP's ERP suite, offering robust asset management capabilities.
Infor EAM: Provides advanced maintenance management and asset optimization.
UpKeep: User-friendly mobile-first CMMS for small to medium-sized businesses.
Fiix: Cloud-based CMMS with a strong focus on usability and integration.

## Slide 32: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
CMMS Architecture and Interface, Use of CMMS
The architecture of a Commercial Computer-Based Maintenance Management System (CMMS) typically involves several layers and components, which work together to provide a robust and scalable platform for managing maintenance operations.
Here's an overview of the common architectural elements:
1. User Interface Layer:
  Web Interface: Accessible via web browsers, allowing users to interact with the CMMS from any location.
  Mobile Interface: Mobile apps for iOS and Android, enabling on-the-go access to the system.
  Desktop Application: In some cases, a dedicated desktop application for offline access.

## Slide 33: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
2. Application Layer:
  Core Modules: Includes the main functional components such as work order management, asset management, preventive maintenance, inventory management, and reporting.
  Business Logic: The rules and processes that govern how data is handled and manipulated within the CMMS.
  APIs: Application Programming Interfaces (APIs) for integration with other systems such as ERP, IoT devices, and SCADA systems.
3. Data Layer:
  Database Management System (DBMS): Centralized database(s) for storing all data related to maintenance activities, assets, inventory, and more.
  Data Warehousing: For historical data storage and complex query processing.
  Data Security: Mechanisms for ensuring data integrity, confidentiality, and availability, including encryption, access controls, and backups.

## Slide 34: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
4. Integration Layer:
  Middleware: Software that facilitates communication and data exchange between the CMMS and other enterprise systems.
  IoT Integration: Connects with IoT devices for real-time monitoring and data collection.
  Third-Party Integrations: Interfaces with third-party applications and services for extended functionality.
5. Infrastructure Layer:
  Cloud Infrastructure: Many modern CMMS solutions are cloud-based, offering scalability, flexibility, and remote access.
  On-Premises Deployment: For organizations that prefer or require hosting the CMMS within their own data centers.
  Networking: Ensures reliable connectivity between the different layers and components of the CMMS.

## Slide 35: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Example of CMMS Interface Design
Here is a conceptual layout of a CMMS interface:
1. Dashboard:
  Top Bar: Navigation menu with links to different modules (e.g., Dashboard, Work Orders, Assets, Inventory, Reports).
  Main Panel: Widgets displaying key metrics (e.g., Open Work Orders, Upcoming PMs, Asset Health).
  Side Panel: Alerts and notifications for critical issues.

## Slide 36: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Let us understand the CMMS more here:
https://www.youtube.com/watch?v=5oHF1PDbWDE

## Slide 37: As learners, we must put more of an emphasis on LISTENING than on working alone!
References: